## Slide 1: Digital Electronics Unit 1-Binary Arithmetic
Dr R THILAK KUMAR
PERIYAR ARTS COLLEGE, CUDDALORE

## Slide 2: BINARY ARITHMETIC
Binary addition
The addition of two binary numbers is very much similar to addition of two decimal numbers. The following rules are followed while adding two binary numbers.
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10 : Read as 0 with carry 1
1 + 1 + 1 = 11 : Read as 1 with carry 1

## Slide 3: Example-1
Add 5 and 6
The equivalent of 5 in binary = 101
The equivalent of 6 in binary = 110
1 (carry)
101 augend
110 addend
1 011

## Slide 4: Example-2
Add 13 and 7
1 1 1 1 (carry)
1 1 0 1
1 1 1
1 0 1 0 0

## Slide 5: Example-3
Add 94 and 125
94 = 5EH = 0101 1110
125 = 7DH = 0111 1101
1 1 1 1
0 1 0 1 1 1 1 0
0 1 1 1 1 1 0 1
1 1 0 1 1 0 1 1
D B

## Slide 6: Binary Subtraction
The subtraction of two binary numbers is similar to the subtraction of two decimal numbers. The following rules are used in subtracting two binary numbers.
0 – 0 = 0
0 - 1 = 1 1 (read as difference 1 with a borrow 1)
1 – 0 = 1
1 - 1 = 0

## Slide 7: Example-1
Subtract 5 from 7
1 1 1 (minuend)
1 0 1 (subtrahend)
0 1 0

## Slide 8: Example-2
Subtract 3 from 13
0 1
1 1 0 1
0 1 1
1 0 1 0

## Slide 9: Example-3
Subtract 14 from 17
1 1 10
1 0 0 0 1
1 1 1 0
0 0 1 1

## Slide 10
11 1 0 1 (5)
1 1 1 (7)
1 1 0 0 (12)

## Slide 11: Binary Multiplication
The following rules are used to multiplay two binary numbers
0 × 0 = 0
0 × 1 = 0
1 × 0 = 0
1 × 1 = 1
It is similar to the decimal multiplication

## Slide 12: Example
Multiply 13 and 11
Binary equivalent of 13 = 1 1 0 1
Binary equivalent of 11 = 1 0 1 1
1 1 0 1 ×
1 0 1 1
----------
1 1 0 1
1 1 0 1
1 0 0 0
1 1 0 1
- ------------------
1 0 0 0 1 1 1 1
--------------------
(8F)H

## Slide 13: Binary division
Binary division has only two rules
0 1 = 0
1 1 = 1
Divide 10 by 4
2 2.5
10 4 10
8 8
------ -------
2 20
------- 20
------
0
-------

## Slide 14
10.1
100 10 10
100 0
-------
100
100
---------
0
----------

## Slide 15: 1’s complement and 2’s complement
Complements are used in digital computers in order to simply the subtraction operation and for the logical manipulations. For the Binary number (base-2) system, there are two types of complements: 1’s complement and 2’s complement.
1’s Complement of a Binary Number
To get 1’s complement of a binary number, simply invert the given number.
2’s Complement of a Binary Number
To get 2’s complement of a binary number, simply invert the given number and add 1 to the least significant bit (LSB) of given result.

## Slide 16: 1’s complement
Binary number | 1’s Complement
1011 | 0100
110001 | 001110
100100 | 011011
11001110 | 00110001
10101101 | 01010010
1111111 | 0000000

## Slide 17: 2’s complement
1’ complement of 1010 = 0101
2’ complemtn of 1010 = 0101
1
------
0 1 1 0

## Slide 18: 2’s complement
Binary number | 1’s complement | 2’s complement
1011 | 0100 | 0101
110001 | 001110 | 001111
100100 | 011011 | 011100
11001110 | 00110001 | 00110010
10101101 | 01010010 | 01010011
1111111 | 0000000 | 0000001

## Slide 19: Subtraction using complements

## Slide 20
1 0 0 0 1
1 0 0 0 1 1 1 1 0 0 1 1 1 0
----------------- + 1 0 0 0 1
1 0 0 0 1 0
1
--------------
0 0 0 1 1

## Slide 21: 2’ complement subtraction
Subtract 18 from 12
12 1 1 0 0 0 1 1 0 0
18 1 0 0 1 0 1 0 0 1 0
---
- 6 1’s complement method
--- 0 1 1 0 0
0 1 1 0 1
1 1 0 0 1
No carry is produced. It indicates that the result is negative. The 1’ s complement is 0 0 1 1 0 = 6