## Slide 1: DIGITAL ELECTRONICS UNIT-1
SIGNED BINARY NUMBERS
&
BINARY CODES

## Slide 2
So far we have used only positive numbers in our discussion. But in everyday practice, we need a method to represent positive numbers as well as negative numbers. In the decimal number system, we use a plus (+) sign to denote positive numbers and a minus (-) sign to denote negative numbers.

## Slide 3
The digital circuits understand only the two binary symbols 0 and 1. Therefore, we have to employ only these two symbols to represent the sign of the number. The usual method is to allot a separate bit to indicate the sign of the number.

## Slide 4
The bit 0 is used to represent (+) or positive numbers and the bit 1 is used to represent (-) or negative numbers. The bit that is used to represent the sign of the number is called the sign bit. The sign bit is the most significant bit (MSB) of a binary number.

## Slide 5
For a positive number, the MSB is equal to 0 and the remaining bits represent the magnitude. This type of representation is called sign-magnitude form. Let us take a few examples with one sign bit and seven bits to represent magnitude.

## Slide 6
DECIMAL | SIGN-MAGNITUDE
+14 | 0 000 1110
-14 | 1 000 1110
+95 | 0 101 1111
-95 | 1 101 1111
+127 | 0 111 1111
-127 | 1 111 1111

## Slide 7
In the sign-magnitude form, another point to note is that 0 is represented as
+0 0 000 0000 and
-0 1 1 0000
The negative numbers are represented with a 1 as sign bit in the MSB position and the magnitude part can be represented in any one of three different ways
1. Sign-magnitude
2. Sign-1’s complement
3. Sign-2’s complement

## Slide 8: Sign-1’ complement
To represent a negative number in 1’s complement form, the following two steps are used.
1. Write the positive binary form of the number, including the sign bit.
2. Invert each bit, including the sign bit, ie.,take 1’s complement
For example, the sign-1’s complement representation for -12 is obtained as follows
+12 = 0 000 1100
-12 = 1 111 0011

## Slide 9
Similarly the sign -1’s complement representation for -93 is obtained as
+93 = 0 101 1101
-93 = 1 010 1110
Similarly the range -127 to + 127 is represented as
+127 = 0 111 1111
-127 = 1 000 0000

## Slide 10: Sign 2’s complement
The sign-2’s complement for -12 is obtained as follows
+ 12 = 0 000 1100
1’s complement of +12 = 1 111 0011
Add 1 1
                -------------------------
                -12 = 1 1 1 1 0 1 0 0
                -------------------------

## Slide 11: Add
+95 and + 27
+ 95 = 0 101 1111 +
+ 27 = 0 001 1011
------ -------------------------
+ 122 0 111 1010
------- --------------------------

## Slide 12
+95 and - 27
+ 95 = 0 101 1111 +
- 27 = 1 110 0101
------ -------------------------
+ 68 1 0 100 0100
------- --------------------------
The carry produced is ignored. The MSB is 0 indicating the result is positive and in true binary form